## Slide 1: SMART INDIA HACKATHON 2026
TITLE PAGE
Problem Statement ID SIH26025
Problem Statement Title Development of an AI-enabled Low Cost Real Time Mine Subsidence Monitoring, Prediction and Early Warning System for Underground Coal Mines in India
Theme Disaster Management
PS Category Hardware
Organisation Ministry of Coal
Team ID [fill after SIH portal]
Team Name WE COOK
Idea MOLE — monitor the model, warn from evidence, inspect on command

## Slide 2
WE COOK
One product: two fixed nodes + laptop ML + one dashboard + a remote rover. Officer sees a change, understands the numbers, then inspects.
1. MONITOR
Node A: tilt + crack slider
Node B: comparison IMU
ESP-NOW → S3-Zero USB JSON
2. WARN + PREDICT
Rules latch WATCH / ALERT
Isolation Forest = unusual
Ridge = next 30 s of signals
3. INSPECT
Operator decides
Rover: FWD REV LEFT RIGHT STOP
Distance, IR, MQ-7 raw, rover IMU
How this maps the PS (honest, tabletop)
PS word | What MOLE actually does | What we do not claim
Monitoring | Live Node A + Node B, source-tagged, timed | Rover IMU is not Node B
Early warning | Rules: 3 samples → WATCH/ALERT; stale → UNKNOWN | Green = healthy data, not a certified-safe mine
AI-enabled | Isolation Forest on this rig’s NORMAL samples; score + top feature on screen | No LLM, no collapse %, no camera vision
Prediction | Ridge: next 30 s of tilt/vibration/crack + MAE | Not a mine-subsidence or roof-fall forecast
Uniqueness | Rules cannot be cleared by ML. A vs B residual = local vs whole-table motion. Rover only after a warning. | Not a gas-car maze robot; not LoRa; not autonomous drive

## Slide 3: TECHNICAL APPROACH
WE COOK
Technologies + method (what is built vs what is claimed)
Layer | Stack | Role
Nodes A/B | Classic ESP32-WROOM-32, MPU6050 I²C 0x68, Node A 10 kΩ slider GPIO34 | Measure tilt, vibration proxy, crack ADC
Receiver | Waveshare ESP32-S3-Zero, ESP-NOW ch1, USB-C JSON 115200 | Bridge only — no sensors, no ML
Laptop ML | Python, Flask, SQLite, scikit-learn IsolationForest + Ridge, joblib | Validate, store, warn, explain
Rover | Classic ESP32, L298N, HC-SR04, IR, MQ-7 raw, Wi-Fi AP Mine-Rover-AP | Remote inspect; separate radio
Node A
Node B
→
S3-Zero
USB JSON
→
Validate
+ features
→
Rules +
IF + Ridge
→
Dashboard
127.0.0.1
→
Rover AP
inspect
Engine | Input (after validation) | Output shown to officer
Rules (latch) | tilt_change, crack mm, freshness, 3 consecutive samples | NORMAL / WATCH (3° or 2 mm) / ALERT (6° or 4 mm) / UNKNOWN (>5 s)
Isolation Forest | ≥120 live NORMAL samples/node; tilt, vib, d_tilt, optional mm, A–B residual | INACTIVE ¦ READY ¦ UNUSUAL + score + top feature
Ridge 30 s | Last ~30 accepted points of the same series | Dashed forecast + MAE. Label: Sensor forecast (30 s). Not a collapse prediction.

## Slide 4: FEASIBILITY AND VIABILITY
WE COOK
Feasible as a tabletop SIH hardware demo: parts in hand, firmware + local website in repo. Field mine certification is out of scope.
Feasibility check | Status
Boards + sensors for A, B, rover, S3-Zero | Available
Node radio | ESP-NOW ch1, tabletop range only
ML on venue laptop | Train 2 min quiet NORMAL before judges
Operator UI | Local Flask, no cloud, no login
Demo loop | Quiet → disturb → WATCH/ALERT → rover → ack
If this happens | Fallback
ESP-NOW / USB drop | UNKNOWN, never fake-green
Not enough NORMAL samples | AI stays INACTIVE; rules still run
Need UI without hardware | --mode simulate, banner on
Rover page dies | Firmware STOP if no cmd ~400 ms
Slider uncalibrated | Node A mm omitted; no fake gap
Risks and how we contain them (no budget theatre)
Risk | Why it is real | Strategy
Over-claiming the PS | Tilt ≠ settlement in cm; IF ≠ collapse probability | Fixed honesty table on dashboard + this PPT
Mixing rover with nodes | Moving IMU would poison Node B / IF | device_id rover; never in node models
False comfort | Disconnected sensor looking healthy | Stale >5 s → UNKNOWN; ML cannot clear a latch
Radio is unencrypted broadcast | Fine for a model; not a mine network | Say tabletop only; no LoRa / mesh claim

## Slide 5: IMPACT AND BENEFITS
WE COOK
Target on demo day: a mine safety officer on a tabletop model. Ministry of Coal is the PS owner. Impact = better notice + evidence + remote look — not disaster prevention numbers we cannot prove.
Who
Officer sees Node A vs Node B, rule reason, AI score, forecast MAE, then drives the rover because a warning appeared.
Social
Fewer unnecessary entries into the model tunnel; decision stays with the human. Ack records awareness; it does not wipe history.
Operational
One laptop website. USB nodes still work if venue Wi-Fi is bad. Rover uses its own AP.
Environment / limits
Hobby electronics on a model. Not intrinsically safe, not DGMS-approved, not a real underground vehicle.
Benefit we can show | How a judge verifies it | Not a benefit we invent
Earlier notice of disturbance | Tilt/slider move → WATCH then latched ALERT in ~3 s | Lives saved / disasters averted
Evidence, not a vibe | Charts + A-vs-B sentence + IF feature + Ridge MAE | 87% collapse risk
Inspect without replacing monitors | Rover telemetry while A/B keep streaming | Autonomous rescue robot
Honest scale path | Same workflow; surveyed mounts + labelled events later | This prototype already predicts subsidence

## Slide 6: RESEARCH AND REFERENCES
WE COOK
References used to design the demo — not proof that MOLE is a certified mine instrument.
Item | Why it is here | Link / citation
PS SIH26025 | Official catalogue ID (not SIH2026025) | SIH 2026 portal / Ministry of Coal, Hardware, Disaster Management
Isolation Forest | Anomaly vs this rig’s normal | Liu, Ting, Zhou — Isolation Forest, IEEE ICDM 2008
Ridge forecast | Short-horizon prediction of measured signals | scikit-learn Ridge; MAE on a held recent window
MPU6050 | Gravity tilt + RMS vibration proxy | InvenSense MPU-6000/6050 Product Specification
ESP-NOW | Node radio on channel 1, tabletop | Espressif ESP-NOW User Guide
ESP32-S3-Zero | USB CDC receiver, no sensors | Waveshare ESP32-S3-Zero wiki
MQ-7 | Rover inspection only, raw ADC | Winsen/Hanwei MQ-7 datasheet — we do not output ppm
Problem domain | Why coal mines care about movement | Ministry of Coal / DGMS published guidance on subsidence & strata — context only
One-line close: MOLE is a working tabletop loop — nodes detect, rules latch, Isolation Forest + Ridge explain, rover inspects.
Upload as PDF. Team ID: fill after portal. Delete no extra slides — this file is already 6.