## Slide 1: SMART INDIA HACKATHON 2026
MOLE
Mine Subsidence Monitoring & Early Warning System
Distributed surface sensing for localized, explainable early warning
•
Problem Statement ID – SIH26025
•
Problem Statement Title-
Development of an AI-enabled Low Cost Real Time Mine Subsidence Monitoring, Prediction and Early Warning System for Underground Coal Mines in India
•
Theme- Disaster Management
•
PS Category- Hardware
•
Team ID-
•
Team Name- We Cook
Current prototype
Notes: Hardware inventory and current deterministic-engine scope: user-supplied request, 29 September 2026. The supplied brief is the authority for the four-node prototype. No physical mine deployment, measurement accuracy, calibration curve or prediction accuracy is asserted. Current ESP-NOW star topology is consistent with firmware/receiver/receiver.ino. Field software labels refer to the proposed field deployment, not a claim that no demo software exists.
The exact SIH26025 problem title and mandatory cover fields are retained from the supplied request.

## Slide 2: MOLE
Proposed Solution: Four nodes. One traceable warning system.
CURRENT PROTOTYPE — 4-NODE HARDWARE DEMONSTRATION
Four-node model
N1
Tilt / vibration
Relative displacement
Moisture context
N2
Tilt / vibration
Temperature context
N3
Relative displacement
MQ-2 context
N4
Tilt / vibration
Local LCD + buzzer
BME280 context
Movement / deformation is the primary evidence. Environmental channels provide context.
Movement
Node
detection
Identified
reading
Gateway
Event /
risk logic
Warning
WHY MOLE IS DIFFERENT
FAULT-AWARE
Failure appears as FAULT / STALE / UNKNOWN, never automatically SAFE.
EXPLAINABLE
Each warning names its node, channel and detected trend or reason.
OFFLINE-FIRST
Local warning remains possible without internet or cloud services.
MULTI-NODE
Planned neighbour corroboration checks isolated spikes before confidence rises.
TARGET USERS
Mine Safety Officers
Survey / Geotechnical Teams
Mine Management
Maintenance / Field Teams
PERIODIC SURVEY
High confidence / periodic
SATELLITE / InSAR
Wide area / periodic
MOLE
Localized / continuous early warning
MOLE complements professional surveying; it does not replace it.
We
Cook
@SIH Idea submission- Template
CURRENT PROTOTYPE
PLANNED FIELD SYSTEM
FUTURE R&D
Notes: Hardware inventory and current deterministic-engine scope: user-supplied request, 29 September 2026. The supplied brief is the authority for the four-node prototype. No physical mine deployment, measurement accuracy, calibration curve or prediction accuracy is asserted. Current ESP-NOW star topology is consistent with firmware/receiver/receiver.ino. Field software labels refer to the proposed field deployment, not a claim that no demo software exists.
MOLE continuously observes localized movement above or near underground workings using distributed sensor nodes and converts abnormal change into traceable early-warning events. N1: ESP32, MPU-class IMU, slide potentiometer, moisture. N2: ESP32, MPU-class IMU, temperature. N3: ESP32, slide potentiometer/linear mechanism, MQ-2. N4: ESP32, MPU-class IMU, BME280, LCD and buzzer. Neighbour agreement remains planned.
Surveying context: https://cimfr.res.in/division/mine-planning-and-surveying.html
Satellite monitoring context: https://www.isro.gov.in/ISRO_EN/NRSC_ISRO_MoU_BCCL_CMPDI.html
MQ-2 is a prototype context channel and does not establish certified mine-gas safety.

## Slide 3: TECHNICAL APPROACH
One architecture — upgraded stage by stage
CURRENT PROTOTYPE
4 ESP32 NODES
Ground movement
+ local conditions
ACQUISITION
Baseline
+ filtering
IDENTIFIED DATA
Node + channel
+ timestamp
ESP-NOW
Direct link
Star topology
ESP32-S3
Receiver / gateway
USB to laptop
RULE / RISK
Threshold, persistence
rate + fault checks
OUTPUT
Local warning
+ laptop monitor
Raw measurements remain separate from risk level. Missing or stale readings reduce confidence.
PLANNED FIELD SYSTEM
Rugged
sensor nodes
LoRa
Edge
gateway
Durable
local storage
Analytics
Database
Dashboard
/ GIS
Remote
alerts
AI ROADMAP
FEATURES
Tilt rate / vibration RMS
Displacement / persistence
Neighbour + environment
SHADOW MODE
Anomaly score only
No alarm override
VALIDATION
Reference data
Held-out field events
AI augments validated deterministic alarms; it does not silently override them.
FUTURE R&D
Predictive models + survey / GNSS / InSAR fusion. Alert-triggered rover adds camera/environment evidence to the same incident record.
Serial log: node / channel / value / quality / time
We
Cook
@SIH Idea submission- Template
CURRENT PROTOTYPE
PLANNED FIELD SYSTEM
FUTURE R&D
Notes: Hardware inventory and current deterministic-engine scope: user-supplied request, 29 September 2026. The supplied brief is the authority for the four-node prototype. No physical mine deployment, measurement accuracy, calibration curve or prediction accuracy is asserted. Current ESP-NOW star topology is consistent with firmware/receiver/receiver.ino. Field software labels refer to the proposed field deployment, not a claim that no demo software exists.
CURRENT: ESP32 / Espressif, Arduino / Embedded C++, actual sensors specified on slide 2. Rule engine: baseline, filtering, thresholds, persistence, rate-of-change, fault/stale detection. Gateway timestamps must distinguish acquisition time from receipt time and record clock quality.
PLANNED: precision displacement sensors, long-range low-data-rate LoRa, Raspberry Pi-class gateway, battery/solar, local durable storage, database, incident history, maintenance diagnostics, dashboard/GIS and SMS/app alerts where suitable. Candidate field stack: FastAPI, PostgreSQL / TimescaleDB, React, Leaflet / OpenStreetMap. These are candidates, not field-deployment claims.
AI: extract tilt rate, vibration RMS/intensity, relative-displacement rate, persistence, cross-node correlation and environmental context. Run an anomaly model in shadow mode before any decision authority. Future predictive models require prototype datasets, historical mine data, field pilot data and independent survey/reference measurements. Validate on held-out sites/events, report missed events, false alarms, lead time and uncertainty without inventing performance.
Future rover sequence: detection, localization of a suspicious zone, authorized verification, then possible rover assistance.
ESP-NOW reference: https://docs.espressif.com/projects/esp-idf/en/stable/esp32/api-reference/network/esp_now.html
LoRaWAN architecture reference (LoRaWAN is a possible network choice, not synonymous with LoRa radio): https://lora-alliance.org/about-lorawan/

## Slide 4: FEASIBILITY AND VIABILITY
Designed to advance through evidence gates
TECHNICAL FEASIBILITY
Four ESP32 sensing nodes
Modular, available components
Node identity + gateway link
Deterministic local processing
Fault visibility + alert capability
Current prototype / implemented element
Sensor limits
Stable IMU mounting. Reference-calibrate sliders before reporting mm. MQ-2 provides context only.
PATH TO FIELD
SCREENING PROTOTYPE
4 nodes + controlled deformation
Gate: repeatable sensing-to-warning test
SURFACE PILOT
LoRa + edge gateway + reference
Gate: packet delivery + reference comparison
HARDENING
Enclosures + power + precision sensors
Gate: weather, power and reliability tests
MINE DEPLOYMENT
Surveyed positions + GIS + maintenance
Gate: site acceptance + applicable approvals
ADVANCED ANALYTICS
Field-trained models + external surveys
Gate: held-out performance + uncertainty
REAL RISKS → ENGINEERING RESPONSE
Sensor drift
Calibration + baseline
Transient noise
Filtering + persistence
False alarm
Planned multi-node corroboration
Node failure
FAULT / STALE / UNKNOWN
Wireless outage
Local logic; planned retries + records
Power failure
Planned battery/solar + health checks
Harsh environment
Planned enclosure + protected mounting
Insufficient mine data
Controlled tests → pilot → validated model
A failed sensor must reduce confidence — it must never silently create a SAFE condition.
Modular commodity nodes enable zone-by-zone deployment and individual node replacement.
We
Cook
@SIH Idea submission- Template
CURRENT PROTOTYPE
PLANNED FIELD SYSTEM
FUTURE R&D
Notes: Hardware inventory and current deterministic-engine scope: user-supplied request, 29 September 2026. The supplied brief is the authority for the four-node prototype. No physical mine deployment, measurement accuracy, calibration curve or prediction accuracy is asserted. Current ESP-NOW star topology is consistent with firmware/receiver/receiver.ino. Field software labels refer to the proposed field deployment, not a claim that no demo software exists.
Evidence gates are acceptance requirements, not claimed completed tests. Commodity components support staged deployment; no bill-of-materials cost, savings percentage or mine approval is asserted. Surface-mounted prototype placement is distinct from equipment approval for a mine operating environment.
DGMS equipment approval context: https://www.dgms.gov.in/writereaddata/UploadFile/APPROVALPOLICY2025_07112025.pdf
BME280 documentation: https://www.bosch-sensortec.com/media/boschsensortec/downloads/datasheets/bst-bme280-ds002.pdf
Professional subsidence and reference surveying: https://cimfr.res.in/division/mine-planning-and-surveying.html

## Slide 5: IMPACT AND BENEFITS
Earlier evidence. Better-informed action.
SAFETY / SOCIAL
Continuous awareness of abnormal local change
Earlier prompt for inspection with a clear reason
Evidence to support safer decisions
OPERATIONAL
Monitoring between periodic surveys
Node/link health distinguishes failure from movement
Planned event history and maintenance diagnostics
DETECT
MOLE sensor
network
VERIFY
Rules + evidence +
authorized safety staff
LOCATE
Node identity
Planned GIS position
INSPECT
Survey / geotechnical
team; future rover assist
RESPOND
Authorized mine
personnel
ECONOMIC
Replace individual nodes as needed
Deploy first in priority zones and expand node by node
Use evidence to target inspection effort
ENVIRONMENT / LAND
Observe land above underground workings
Flag zones needing closer inspection
Planned GIS assets; future remote-sensing fusion
Decision support — field action remains with authorized mine personnel and approved safety procedures.
We
Cook
@SIH Idea submission- Template
CURRENT PROTOTYPE
PLANNED FIELD SYSTEM
FUTURE R&D
Notes: Hardware inventory and current deterministic-engine scope: user-supplied request, 29 September 2026. The supplied brief is the authority for the four-node prototype. No physical mine deployment, measurement accuracy, calibration curve or prediction accuracy is asserted. Current ESP-NOW star topology is consistent with firmware/receiver/receiver.ino. Field software labels refer to the proposed field deployment, not a claim that no demo software exists.
Benefits describe the intended operational value, not measured field outcomes. No claim of preventing all incidents, predicting collapse accurately, eliminating accidents, or quantified savings. The central response workflow describes human decision support. Planned field capabilities include maintenance diagnostics, durable incident history and surveyed GIS positions. Rover inspection and remote-sensing fusion remain future R&D.

## Slide 6: RESEARCH AND REFERENCES
Source → engineering decision
DOMAIN RESEARCH
Official SIH26025
Exact problem scope
CSIR-CIMFR Mine Planning & Surveying
Indian subsidence / geotechnical monitoring
ISRO / NRSC / BCCL / CMPDI
Remote sensing and coalfield monitoring
DGMS approval policy
Mine equipment and safety approval context
Espressif ESP32 / ESP-NOW
Current direct wireless link and receiver
Bosch Sensortec BME280
Environmental sensor limits and documentation
LoRa Alliance
Planned field-network architecture reference
PEER-REVIEWED SUBSIDENCE PAPERS
PROTOTYPE PROOF
WORKING PROTOTYPE VIDEO
Movement → detection → data transfer
→ warning → fault test
2–3 minute demonstration
GITHUB / ENGINEERING EVIDENCE
Firmware, wiring and architecture
Test logs and prototype photographs
Calibration and limitations
Measured result / FAULT–STALE or LCD evidence
We
Cook
@SIH Idea submission- Template
CURRENT PROTOTYPE
PLANNED FIELD SYSTEM
FUTURE R&D
Notes: Hardware inventory and current deterministic-engine scope: user-supplied request, 29 September 2026. The supplied brief is the authority for the four-node prototype. No physical mine deployment, measurement accuracy, calibration curve or prediction accuracy is asserted. Current ESP-NOW star topology is consistent with firmware/receiver/receiver.ino. Field software labels refer to the proposed field deployment, not a claim that no demo software exists.
Sources inspected on 29 September 2026:
sih: https://sih.gov.in/
cimfr: https://cimfr.res.in/division/mine-planning-and-surveying.html
isro: https://www.isro.gov.in/ISRO_EN/NRSC_ISRO_MoU_BCCL_CMPDI.html
dgms: https://www.dgms.gov.in/writereaddata/UploadFile/APPROVALPOLICY2025_07112025.pdf
esp: https://docs.espressif.com/projects/esp-idf/en/stable/esp32/api-reference/network/esp_now.html
bosch: https://www.bosch-sensortec.com/media/boschsensortec/downloads/datasheets/bst-bme280-ds002.pdf
lora: https://lora-alliance.org/about-lorawan/
SIH problem-statement wording comes from the supplied brief. The portal link is general; the exact 2026 entry was not independently located. LoRa Alliance describes LoRaWAN network architecture; selecting LoRa radio does not automatically mean adopting LoRaWAN.
No peer-reviewed papers are attributed to the team without confirmation that they have read them. No fabricated calibration plots, logs, footage, QR destinations or physical tests.