## Slide 1: SMART INDIA HACKATHON 2026
TITLE PAGE
MOLE · Mine Observation & Live-alert Engine
Problem Statement ID – SIH26025
Problem Statement Title – Development of an AI-enabled Low Cost Real Time Mine Subsidence Monitoring, Prediction and Early Warning System for Underground Coal Mines in India
Theme – Disaster Management
PS Category – Hardware
Team ID – To be assigned on the SIH portal after college shortlist
Team Name – WE COOK

## Slide 2: MOLE
Proposed solution · how it addresses SIH26025 · what is unique
WE COOK
1 Nodes A + B
Watch continuously
2 Rules + AI
Flag unusual change
3 Dashboard
Show the evidence
4 Operator
Decide to inspect
5 Rover
Look, then report
Isolation Forest is early anomaly detection — a precursor stage toward prediction. It does not output a collapse probability.
What MOLE does for SIH26025
• Node A watches surface tilt vs a captured baseline.
• Node B watches vibration / disturbance at a second point.
• Watch / Alert latch with a written reason and history.
• Rover inspects only after the operator decides — it is not the monitor.
• One local dashboard. Rover vibration is never treated as Node B.
Why this is not a copy of other student kits
• Walk-in checks send a person in first. Nodes keep watching.
• InSAR / surveys are slow for a heading. This is a live tabletop loop.
• Rover-only kits have no standing surface watch.
• Unexplained AI scores hide the reason. Rules and AI are shown separately.
Scientific basis (proxy, not a geophone)
• MPU6050 tilt and vibration are low-cost proxies for mounting-surface micro-movement. They are not professional microseismic arrays.
• Published Indian longwall work: microseismic event-rate changes can precede roof / ground failure (Sivakumar et al., 2005, Rajendra / SECL).
• DGMS (S&T) Tech. Circular 01 of 2017, cl. 6.1 asks longwall mines for surface geophones. That is field-grade method — not this tabletop prototype.
Stakes: CIL recorded 22 fatal accidents and 24 fatalities in 2024 up to November (MoC Annual Report 2024-25, Ch.14, Table 2; subject to DGMS reconciliation). Strata / roof control remains a named underground safety focus.

## Slide 3: TECHNICAL APPROACH
Technologies · methodology · working prototype
WE COOK
Hardware (tabletop prototype)
• Node A: ESP32-WROOM-32 + MPU6050 for tilt / movement.
• Node B: ESP32-WROOM-32 + MPU6050 for vibration.
• Rover: motors + driver, remote FWD / REV / LEFT / RIGHT / STOP.
• USB ESP32 gateway: radio/serial infrastructure, not a fourth node.
• Parts are already with the team. This is a demonstration rig, not mine-certified gear.
Software (one laptop)
• Python dashboard. SQLite event history.
• Rules: Watch / Alert after 3 consecutive samples; 5 s stale → UNKNOWN.
• AI: scikit-learn Isolation Forest vs learned normal. Anomaly detector only.
• AI cannot clear a rule alert. If untrained, show INACTIVE.
• Every reading is source-tagged and timed.
Communication
• Prototype, surface nodes: ESP-NOW to the USB gateway.
• Rover commands use a separate control path. Not the node radio.
• Not claimed: underground Wi-Fi / ESP-NOW range through rock or coal.
• Field path (after an RF survey): LoRa, mesh, repeater, leaky-feeder, or mine-approved infrastructure — future work, not this demo.
Method, every accepted reading
• Is the packet fresh, valid, and from a known device ID?
• Compute change from the captured baseline (tilt / vibration).
• Demand persistence — one tap is not an alert.
• Run rules and Isolation Forest. Never let AI override a rule.
• Show the reason. If the officer decides, send the rover and log it.
• 1 Hz firmware design. Latency and radio range: TBD — test pending.

## Slide 4: FEASIBILITY AND VIABILITY
Feasibility · challenges and risks · how we handle them
WE COOK
Build now
Two surface nodes, USB gateway, laptop dashboard, remote rover.
Isolation Forest on live baseline samples.
Local only — no cloud dependency for the demo.
Honest limit
A tabletop model is not a mine.
Tilt is orientation, not centimetres of settlement.
Green means healthy data, not a certified-safe mine.
Field path
Surveyed mounts and site-calibrated thresholds.
DGMS-approved / certified sensing and comms.
Collapse models need geotech / InSAR labels we do not have.
Risks we already design for
• False green: a missing packet can look fine. After 5 s stale → UNKNOWN, never NORMAL.
• One noisy sample (tap, wire tug): require 3 consecutive samples before Watch / Alert.
• Rover IMU mistaken for Node B: same sensor family, different job. Device ID on every reading.
• ESP32 ADC2 fights wireless: crack slider only on GPIO34 / ADC1, or drop millimetre claims.
• AI over-claim on a short tabletop set: Isolation Forest cannot clear a rule alert.
• Unlinked crack knob is not a gap: two-point ruler scale, or do not quote millimetres.
• Venue Wi-Fi / cloud demos die: laptop-local dashboard; backup video ready.
• COTS ESP32 / MPU6050 are not intrinsically safe. Tabletop only. Underground use needs DGMS-approved equipment for that hazardous area.

## Slide 5: IMPACT AND BENEFITS
Who it is for · what we can honestly claim · what comes next
WE COOK
Who this helps
• Mine safety officer: evidence, written reason, and history — not a serial dump.
• Inspection crew: rover goes in after Watch / Alert; nodes keep watching.
• College / SIH judges: live loop — disturb → warn → inspect → log.
• Later mine operator: same dashboard language; certified sensors can replace hobby heads.
Benefits we will actually stand behind
• Social: fewer unnecessary entries into a disturbed heading on the demo analogue.
• Economic: a standing ESP32-class watch vs waiting for a specialist survey.
• Disaster: earlier notice of surface tilt and vibration — the PS proxy for subsidence, not proof of collapse.
• User experience: colour status, charts, written reason, rover pad. Acknowledging an alert does not erase the event.
Status discipline on the dashboard
NORMAL / WATCH / ALERT / UNKNOWN. Stale or missing telemetry → UNKNOWN, never false NORMAL. Green means healthy data. It does not mean a certified-safe mine. Rover is secondary inspection, idle until requested.
NOW
Tabletop nodes + rover + local dashboard.
NEXT
More calibrated nodes, spatial view, extended validation.
FIELD
Surveyed mounts, site thresholds, DGMS-approved sensing / comms, mine monitoring integration.

## Slide 6: RESEARCH AND REFERENCES
References · what we will show on 10 September
WE COOK
Sources actually used
1. Coal Mines Regulations, 2017 · DGMS — duty to report dangerous occurrences.
2. SIH 2026 · SIH26025 · Ministry of Coal · Hardware.
3. MoC Annual Report 2024-25, Ch.14, Table 2 — CIL accident counts to Nov 2024 (not a cause-share %).
4. Liu, Ting, Zhou — Isolation Forest, ICDM 2008. Library: scikit-learn IsolationForest.
5. TDK / InvenSense MPU-6000/6050 datasheet — tilt / vibration sensor limits.
6. Espressif ESP-NOW and ESP32 ADC docs — node radio; ADC1 vs wireless wiring.
7. Sivakumar C., Srinivasan C., Gupta R.N. (2005) RaSiM 6 — Rajendra Colliery / SECL microseismic case.
8. DGMS (S&T) Tech. Circular No. 01 of 2017, cl. 6.1 — longwall geophones; not implemented here.
9. SBAS-InSAR literature — later fusion path only, not claimed as built.
If a judge has seen bigger claims on other SIH decks
• “AI predicts mine collapse %” → Isolation Forest on tabletop normal data + rule thresholds.
• “LoRa mesh across a colliery” → ESP-NOW on the tabletop. LoRa is not demonstrated.
• “Autonomous rover / AI vision” → remote drive. Camera only if shown live.
• “Green = the mine is safe” → green = healthy data, no configured trigger.